## Slide 1: Very Brief Introduction about How to Use MIRO

## Slide 2: Using MIRO
Start the CORBA Naming Service
Select Available MIRO Services
  SICK Laser
  Encoder
  GPS
  Map/3D Map
Subscribe to events

## Slide 3: Event Channel
Publish
Subscribe

## Slide 4: Makefile
Generated from makefile.am
configure.ac is where you add new source/folders to be compiled
Need to run ./configure and ./bootstrap

## Slide 5: Sample makefile.am
## Makefile.am
## ** CopyRight(c) 2009: COBRA Research Group & DRDC - Atlantic
## **
## ** Electrical and Computer Engineering,
## ** University of New Brunswick,
## ** Fredericton, NB, Canada
## **
## ** Author: Revision by Howard Li
##
include $(top_srcdir)/config/Make-rules
INCLUDES = $(ATLAS_CPPFLAGS)
AM_LDFLAGS += $(ATLAS_LDFLAGS)
## binaries to be built
bin_PROGRAMS = OceanService
## sourcefiles needed for the different binaries to be built
## the prefix of the following macros must have the same name as the respective binary
OceanService_SOURCES = \
Parameters.xml \
RangePushConsumer.cpp \
OceanBase.cpp \
TerrainMap.cpp \
TerrainElevMap.cpp \
TerrainMapDefs.h \
OceanPose.cpp
BUILT_SOURCES = Parameters.cpp Parameters.h
CLEANFILES = $(BUILT_SOURCES)
## libraries that need to be linked for the bin_PROGRAMS to compile
OceanService_LDADD = \
$(MIRO_ROOT)/lib/libmiroSvc.a \
-lmiroIDL \
-lDrdcIDL \
-lmiro \
-ldrdcmiro \
-llapack \
-lcblas \
-latlas
all-local:
$(INSTALLPROGRAMS)
clean-local:
$(CLEANPROGRAMS)

## Slide 6: Sample XML File
## ** CopyRight(c) 2009: COBRA Research Group & DRDC - Atlantic
## **
## ** Electrical and Computer Engineering,
## ** University of New Brunswick,
## ** Fredericton, NB, Canada
## **
## ** Author: Revision by Howard Li
##
<!DOCTYPE xml SYSTEM "PolicyEditor_behaviour.dtd">
<config>
<config_global name="namespace" value="Ocean" />
<config_global name="include" value="miro/SvcParameters.h" />
<config_global name="include" value="miro/eventParameters.h" />
<config_global name="include" value="miro/TransformParameters.h" />
<config_global name="include" value="idl/MapDescriptionC.h" />
<config_global name="include" value="idl/MapC.h" />
<config_global name="include" value="miro/MapDescriptionHelper.h" />
<config_group name="OceanMapConfig">
<config_item parent="Miro::Config" instance="true">
<config_parameter name="notify" type="bool" default="true" />
<config_parameter name="useShared" type="bool" default="false" />
<config_parameter name="eventChannelDescription" type="Miro::EventChannelParameters"/>
<config_parameter name="mapDescription" type="Miro::MapDescriptionIDL" />
<constructor>
mapDescription.eventName = "Ocean";
mapDescription.mapType = Miro::Map::TERRAIN_MAP_SEQ;
mapDescription.depth = 40000;
mapDescription.width = 40000;
mapDescription.gridsize = 400;
</constructor>
<config_parameter name="sonarTransformDescription" type="Miro::TransformListParameters"/>
<config_parameter name="mapEventInterval" type="double" default="0.25" />
<config_parameter name="mapUpdateTime" type="double" default="7.0" />
<config_parameter name="bumperHeight" type="double" default="0" />
<config_parameter name="maxVelocity" type="int" default="20000" />
<config_parameter name="poseInterval" type="double" default="1" />
<config_parameter name="orientationDevError" type="double" default="2.0" />
<config_parameter name="stereoPeriod" type="double" default="0.5" />
</config_item>
</config_group>
</config>

## Slide 7: Procedure
0. create softlinks for Naming_Service and nslist
su cd /usr/local/bin ln -s /usr/local/ACE/TAO/orbsvcs/Naming_Service/Naming_Service . ln -s /usr/local/ACE/TAO/utils/nslist/nslist . exit 1. change to your home directory cd ~/ 2. start the Naming Service Naming_Service $NS 3. cd ~/ulmMiro/bin 4. start the logplayer ./LogPlayer <logfilename> 5. write your own MIRO service to publish events to the event channel 6. start the service